## Slide 1: Time Domain Analysis of Linear Systems Ch2
University of Central Oklahoma
Dr. Mohamed Bingabr

## Slide 2: Outline
Zero-input Response
Impulse Response h(t)
Convolution
Zero-State Response
System Stability

## Slide 3: System Response
Initial Conditions
are not zeros
(stored energy)
x(t) = 0
y(t) = zero input response
System
Initial Conditions
are zeros
(No stored energy)
x(t)
y(t) = zero state response
System
Total response = Zero input response + Zero state response

## Slide 4: System Response
What is the zero-input response?
For N order system

## Slide 5: Zero-Input Response
A solution to the above differential equation is
Characteristic Equation
Characteristic Polynomial

## Slide 6: Zero-Input Response
A general solution of the zero-input response is
If the characteristic roots λs are distinct real, then possible solutions to the differential equation are
Next step is to solve the characteristic equation

## Slide 7: Zero-Input Response
The zero-input response is
Characteristic Modes: … , determine the system’s behavior
Characteristic Roots: λ1 … λN
- Also called the natural frequencies or eigenvalues
- For stable system all λ ≤ 0
- Can be real distinct, repeated roots, and/or complex roots
The constants c1, …, cn are arbitrary constants that will be determined by the initial conditions (initial states of the system)

## Slide 8: Example
For the LTI system described by the following differential equation (D2 + 3D + 2) y(t) = D x(t)
The initial conditions are y(0) = 0 and
Find
The characteristic equation
The characteristic roots
The characteristic modes
The zero-input response
Answer:

## Slide 9: Repeated Characteristic Roots
If the characteristic equation
,
has this form
then the N characteristic roots has the same value λ1.
The zero-input solution will be

## Slide 10: Example
For the LTI system described by the following differential equation (D2 + 6D + 9) y(t) = (3D +5) x(t)
The initial conditions are y(0) = 3 and
Find
The characteristic equation
The characteristic roots
The characteristic modes
The zero-input response
Answer:

## Slide 11: Complex Characteristic Roots
If the characteristic equation
has a complex characteristic root σ + jω then its conjugate σ - jω is also a characteristic root. This is necessary for the system to be physically realizable.
The zero-input solution for a pair of conjugate roots is
If c1 and c2 are complex, then c2 is conjugate of c1.

## Slide 12: Example
For the LTI system described by the following differential equation (D2 + 4D + 40) y(t) = (D +2) x(t)
The initial conditions are y(0) = 2 and
Find
The characteristic equation
The characteristic roots
The characteristic modes
The zero-input response
Answer: or

## Slide 13: The Meaning of t = 0- and t = 0+
y(0-): At t = 0- the input is not applied to the system yet so the output is due only to the initial conditions.
t = 0
x(t)
y(t)
System
y(0+): At t = 0+ the input is applied to the system, so the output is due the input and the initial conditions.

## Slide 14: Impulse Response h(t)
x(t) = (t)
y(t) = h(t)
LTI
System

## Slide 15: Unit Impulse Response h(t)
Reveal system behavior
Depends on the system internal characteristic modes
Helps in finding system response to any input x(t)

## Slide 16: Derivation of Impulse Response h(t)
1- Find the differential equation of the system
2- Find the natural response yn(t) using the same steps used to find the zero-input response.
3- To find the constants c, set all initial conditions to zeros except N-1 derivative, set it to equal 1.
4-
If M = N then h(t) = [P(D) yn(t)] u(t) + b0 (t)
Q(D)
P(D)
x(t)
h(t)

## Slide 17
Example
Determine the impulse response h(t) for the system
(D2 + 3D + 2) y(t) = (D +3) x(t)
Answer:
HW3_Ch2

## Slide 18: Zero-State Response
x(t)
y(t) = x(t) * h(t)
LTI
h(t)
convolution

## Slide 19
Zero-State Response
Any signal can be represented as a train of pulses of different amplitudes and at different locations

## Slide 20
Zero-State Response
x(t)
y(t)
Each curve represents the output for impulse input at nΔt
y(t) is the sum of all curves.
Input x(t)

## Slide 21
Zero-State Response
x(t)
y(t) = x(t) * h(t)
h(t)
y(t) = h(t) * x(t)
The Convolution Integral

## Slide 22
Example
For a LTI system with impulse response h(t) = e-2t u(t), determine the response y(t) for the input x(t) = e-t u(t).
Answer:
=

## Slide 23
The Convolution Properties
Commutative: x1 * x2 = x2 * x1
Associative: x1 * [x2 * x3] = [x1 * x2 ] * x3
Distributive: x1 * [x2 + x3] = [x1 * x2 ] + [x1 * x3 ]
Impulse Convolution: x(t) * (t) = x(t)

## Slide 24
The Convolution Properties
Shift Property:
if x1(t) * x2(t) = c(t)
then x1(t -T) * x2(t) = x1(t) * x2(t -T) = c(t -T)
also x1(t –T1) * x2(t –T2) = c(t –T1 –T2)
Width Property:
If the width of x1(t) is T1 and the width of x2(t) is T2
then the width of x1(t ) * x2(t) is T1 +T2

## Slide 25
Find the total response for the system D2y + 3Dy + 2y = Dx for input x(t)=10e-3tu(t) with initial condition y(0) = 0 and
Answer
Example
For t  0
Zero-input Response
Zero-state Response
Natural Response
Forced Response

## Slide 26: System Stability
External Stability (BIBO)
  If the input is bounded, then the output is bounded
Internal Stability (Asymptotic)
  If and only if all the characteristic roots are in the LHP
  Unstable if, and only if, one or both of the following conditions exist:
    At least one root is in the RHP
    There are repeated roots on the imaginary axis
  Marginally stable if, and only if, there are no roots in the RHP, and there are some unrepeated roots on the imaginary axis.

## Slide 27: Example
Investigate the asymptotic & BIBO stability of the following systems:
(D+1)(D2 + 4D + 8) y(t) = (D - 3) x(t)
(D-1)(D2 + 4D + 8) y(t) = (D + 2) x(t)
(D+2)(D2 + 4) y(t) = (D2 + D + 1) x(t)
HW4_Ch2

## Slide 28: Convolution Example
Find the zero-state response y(t) of the system described by the impulse response h(t) for an input x(t), shown below.
2
h(t)
4
t
2t
x(t)
4
0
2
t

## Slide 29: Convolution Example
2
x(t)
4
0
h(t)
4
2
Find the zero-state response y(t) of the system described by the impulse response h(t) for an input x(t), shown below.
t
t
x(-)
-4
0
2

x(t-)
t
t - 4
2t
2
h()
4

0
2
2

## Slide 30: Convolution Demonstration
x(t-)
t
t - 4
2
h()
4

0
2
2
y(t) for t < 0

## Slide 31: Convolution Demonstration
x(t-)
t
t - 4
0
y(t) for 0 < t < 2

## Slide 32: Convolution Demonstration
x(t-)
t
t - 4
2
h()
4

0
2
2
y(t) for 2 < t < 4

## Slide 33: Convolution Demonstration
x(t-)
t
t - 4
2
h()
4

0
2
2
y(t) for 4 < t < 6

## Slide 34: Convolution Demonstration
x(t-)
t
t - 4
2
h()
4

0
2
2
y(t) for t > 6