## Slide 1
Engineering and Physics
University of Central Oklahoma
Dr. Mohamed Bingabr
Ch6
Continuous-Time Signal Analysis
ENGR 3323: Signals and Systems

## Slide 2: Outline
Introduction
Fourier Series (FS) Representation of Periodic Signals.
Trigonometric and Exponential Form of FS.
Gibbs Phenomenon.
Parseval’s Theorem.
Simplifications Through Signal Symmetry.
LTIC System Response to Periodic Inputs.

## Slide 3: Sinusoidal Wave and phase
x(t) = Asin(t) = Asin(250t)
A
t
T0 = 20 msec
x(t)
A
t
td = 2.5 msec
x(t-0.0025)= Asin(250[t - 0.0025])
= Asin(250t - 0.25)= Asin(250t - 45o)
Time delay td = 2.5 msec correspond to phase shift  = 45o

## Slide 4: Representation of Quantity using Basis
Any number can be represented as a linear sum of the basis number {1, 10, 100, 1000}
Ex: 10437 =10(1000) + 4(100) + 3(10) +7(1)
Any 3-D vector can be represented as a linear sum of the basis vectors {[1 0 0], [0 1 0], [0 0 1]}
Ex: [2 4 5]= 2 [1 0 0] + 4[0 1 0]+ 5[0 0 1]

## Slide 5: Basis Functions for Time Signal
Any periodic signal x(t) with fundamental frequency 0 can be represented by a linear sum of the basis functions {1, cos(0t), cos(20t),…, cos(n0t), sin(0t), sin(20t),…, sin(n0t)}
Ex:
x(t) =1+ cos(2t)+ 2cos(2 2t)+ 0.5sin(23t)+ 3sin(2t)

## Slide 6
x(t) =1+ cos(2t)+ 2cos(2 2t)+ 3sin(2t)+ 0.5sin(23t)
+
+
+
=

## Slide 7: Purpose of the Fourier Series (FS)
FS is used to find the frequency components and their strengths for a given periodic signal x(t).

## Slide 8: The Three forms of Fourier Series
Trigonometric Form
Compact Trigonometric (Polar) Form.
Complex Exponential Form.

## Slide 9: Trigonometric Form
It is simply a linear combination of sines and cosines at multiples of its fundamental frequency, f0=1/T.
a0 counts for any dc offset in x(t).
a0, an, and bn are called the trigonometric Fourier Series Coefficients.
The nth harmonic frequency is nf0.

## Slide 10: Trigonometric Form
How to evaluate the Fourier Series Coefficients (FSC) of x(t)?
To find a0 integrate both side of the equation over a full period

## Slide 11: Trigonometric Form
To find an multiply both side by cos(2mf0t) and then integrate over a full period, m =1,2,…,n,…
To find bn multiply both side by sin(2mf0t) and then integrate over a full period, m =1,2,…,n,…

## Slide 12: Example
Fundamental period
  T0 = p
Fundamental frequency
  f0 = 1/T0 = 1/p Hz
  w0 = 2p/T0 = 2 rad/s
0
p
-p
1
e-t/2
f(t)
To what value does the FS converge at the point of discontinuity?

## Slide 13: Simplifications Through Signal Symmetry
If x (t) is EVEN: It must contain Cosine Terms and it may contain DC. Hence bn = 0.
If x(t) is ODD: It must contain ONLY Sines Terms. Hence a0 = an = 0.

## Slide 14
A periodic signal x(t), has a Fourier series if it satisfies the following conditions:
x(t) is absolutely integrable over any period, namely
x(t) has only a finite number of maxima and minima over any period
x(t) has only a finite number of discontinuities over any period
Dirichlet Conditions

## Slide 15
Using single sinusoid,
are related to the trigonometric coefficients an and bn as:
and
Compact Trigonometric Form
The above relationships are obtained from the trigonometric identity
a cos(x) + b sin(x) = c cos(x + )

## Slide 16
Compact Trigonometric Form
a cos(x) + b sin(x) = c cos(x + )

## Slide 17
Role of Amplitude in Shaping Waveform

## Slide 18
Role of the Phase in Shaping a Periodic Signal

## Slide 19: Compact Trigonometric
Fundamental period
  T0 = p
Fundamental frequency
  f0 = 1/T0 = 1/p Hz
  w0 = 2p/T0 = 2 rad/s
0
p
-p
1
e-t/2
f(t)

## Slide 20
The amplitude spectrum of x(t) is defined as the plot of the magnitudes |Cn| versus 
The phase spectrum of x(t) is defined as the plot of the angles versus 
This results in line spectra
Bandwidth as the difference between the highest and lowest frequencies of the spectral components of a signal.
Line Spectra of x(t)

## Slide 21: Line Spectra
0
p
-p
1
e-t/2
f(t)
f(t)=0.5 + 0.24 cos(2t-76o) + 0.12 cos(4t-82.9o) +
0.08 cos(6t-85.2o) + 0.06 cos(8t-86.2o) + …
0.5
0.24
0.12
0.08
0.06
Cn

0 2 4 6 8 10

n
-/2
0 2 4 6
0.05

## Slide 22
x(t) can be expressed as
D-n = Dn*
Exponential Form
To find Dn multiply both side by and then integrate over a full period, m =1,2,…,n,…
Dn is a complex quantity in general Dn=|Dn|ej
Even
Odd
|Dn|=|D-n|
Dn = - D-n
D0 is called the constant or dc component of x(t)
&

## Slide 23
The line spectra for the exponential form has negative frequencies because of the mathematical nature of the complex exponent.
Line Spectra of x(t) in the Exponential Form
Cn = 2|Dn|
Cn = Dn
C0 = D0

## Slide 24: Example
/2
-/2
1
f(t)
-To
To
Find the exponential Fourier Series for the square-pulse periodic signal.
To/2
-To/2
If To = 2 and  =  then

## Slide 25
/2
-/2
1
f(t)
-To
To
To/2
-To/2

## Slide 26
Exponential Line Spectra

## Slide 27
Gibbs Phenomenon

## Slide 28
overshoot: about 9 % of the signal magnitude (present even if )
Gibbs Phenomenon – Cont’d

## Slide 29: Example
Find the exponential Fourier Series and sketch the corresponding spectra for the impulse train shown below. From this result sketch the trigonometric spectrum and write the trigonometric Fourier Series.
2T0
T0
-T0
-2T0
Solution

## Slide 30
Relationships between the Coefficients of the Different Forms

## Slide 31
Let x(t) be a periodic signal with period T
The average power P of the signal is defined as
Expressing the signal as
it is also
Parseval’s Theorem

## Slide 32: LTIC System Response to Periodic Inputs
H(s)
H(j)
A periodic signal x(t) with period T0 can be expressed as
For a linear system
H(s)
H(j)

## Slide 33: Fourier Series Analysis of DC Power Supply
A full-wave rectifier is used to obtain a dc signal from a sinusoid sin(ω1t). The rectified signal x(t) is applied to the input of a lowpass RC filter, which suppress the time-varying component and yields a dc component with some residual ripple. Find the filter output y(t). Find also the dc output and the rms value of the ripple voltage.

## Slide 34
for ω0 = 2
Ripple rms is only 5% of the input amplitude
Fourier Series Analysis of DC Power Supply

## Slide 35
clear all
t=0:1/1000:3*pi;
for i=1:100
n=i;
yp=(2*exp(j*2*n*t))/(pi*(1-4*n^2)*(j*6*n+1));
n=-i;
yn=(2*exp(j*2*n*t))/(pi*(1-4*n^2)*(j*6*n+1));
y(i,:)=yp+yn;
end
yf = 2/pi + sum(y);
plot(t,yf, t, (2/pi)*ones(1,length(yf)))
axis([0 3*pi 0 1]);
Power=0;
for n=1:50
Power(n) = abs(2/(pi*(1-4*n^2)*(j*6*n+1)));
end
TotalPower = 2*sum((Power.^2));
figure; stem( Power(1,1:20));
This Matlab code will plot y(t) for -100  n  100 and find the ripple power according to the equations below
Fourier Series Analysis of DC Power Supply